## Slide 1
Quizz #2
Mardi 4 Decembre 2018

## Slide 2: Question #1
What diameter will the tennis ball have that is used to check, if a vehicle complies to the "Open Wheel" definition?
70 mm
72.5 mm
75 mm
80 mm
Notes: 68.6

## Slide 3: Question #2
Which frame component does not necessarily belong to the primary structure?
Suspension Mounting Points
Front Bulkhead
Side Impact Structure
Front Hoop
Notes: Suspension

## Slide 4: Question #3
Which of these measures is not used to dimension the external part of cockpit opening template ?
50mm
100mm
75mm
350mm
Notes: 50mm

## Slide 5: Question #4
What is the minimum width of a head restraint with a height of 200mm
150mm
117.5mm
50mm
280mm
Notes: 150mm

## Slide 6: Question #5
In order to test, if the vehicle provides sufficient overall stability for cornering with 1.7G, it is tilted to 60° on the tilt table. To which angle must the vehicle be tilted to simulate cornering with 2.5G?
68.2°
65.0°
67.8°
69.1°
Notes: 68.2

## Slide 7: Question #6 a refaire
The space needed for the technical inspection sticker at FSG is approximately
254mm wide x 203mm high
203mm wide x 254mm high
75mm high x 150mm wide
150mm high x 75mm wide
Notes: 75h*150w

## Slide 8: Question #7
How far must throttle cables at least be apart from any exhaust system component?
50 mm
25 mm
75 mm
100 mm
Notes: 50.8

## Slide 9: Question #8
What is the sum of the maximum scores of all static events?
325 pts
300 pts
350 pts
275 pts
Notes: 325

## Slide 10: Question #9
The quick jack must be able to lift up the car, so that the driven wheels are at least :
10 cm
12.5 cm
15 cm
18 cm
Notes: 10.2

## Slide 11: Question #10
The front track of a vehicle is 1350mm wide. What is the difference of the maximum and minimum allowed width of the rear track?
756.833mm
757.25mm
756.53mm
756.821mm
779mm
Notes: .833