## Slide 1
Quizz #2
Mardi 4 Decembre 2018

## Slide 2: Question #1
What is the minimum distance between 95th percentile lower 200mm circle and face of the pedal ?
925 mm
920 mm
37 in
36 in
Notes: 36 in

## Slide 3: Question #2
What is the maximum angle which the lower portion of Main hoop (i-e below upper side impact member) can make with the horizontal, when inclined rearward ?
No limit
10
80
45
Notes: 80

## Slide 4: Question #3
The engine lubrication system of your vehicle has a capacity of 12.5l. In driving condition it is 80% filled with the fluid. What is the minimum volume of catch can?
1l
0.9l
1.1l
1.2l
Notes: 1l

## Slide 5: Question #4
Which ones meets the positive locking requirement?
Washers
Cotter pins
Bolts with nylon patches
Loctite
Notes: Cotter pins

## Slide 6: Question #5
Runner system between restrictor and throttle body is made up of rectangular cross-section with height 55mm. What is the possible width of the runner system?
60mm
50mm
55mm
65mm
Notes: 50mm

## Slide 7: Question #6
What is the penalty, if a team is not able to submit notice of intent or FMEA of ETC by the due date?
-10 points daily till max -50 points
Disqualification from competition
Back to mechanical throttle
No penalty
Notes: Back to mechanical throttle

## Slide 8: Question #7
Which of the following is not a requirement of Cost report ?
Font size 10 point or higher
Page size A4
Page size 8.5in x 11in
Must not exceed 350 pages
Notes: Must not exceed

## Slide 9: Question #8
In Autocross Event, which flag is used to indicate the approval to begin ?
Blue flag
Red flag
Green flag
Red-yellow striped
Notes: green

## Slide 10: Question #9
In endurance event if a team exceeds Tmax time then how much points do they score ?
50
25
10
0
Notes: 25

## Slide 11: Question #10
Which of the following act results in penalty ?
Alcohol and illegal material
Arguments with official
Unsportsmanlike conduct
Failed to follow an official instruction
Notes: Failed to follow